## Slide 1
Jakob Roberts
Bogdan Fanea
Scott Andreen
Need
The frequency of unretained deropements of surface
lifts in BC is unacceptably high.
Goal
Improve current surface lifts to increase the safety in regards to deropements involving snowboarders.
Objectives
Doesn’t slow current operating speed
Inexpensive solution
Low implementation time
Simple to use for the general public.
Constraints
Can’t add >20% of current weight to system.
New design is compatible with older systems.
Resistance against all elements causing corrosion or failure of components.
Background Info
Current T-bar design and alternatives are flawed for snowboarder use.
Connection design between T-bar, attachment cable, and main lift cable causes deropements from horizontal force.
BCSA representatives claim minimal research into reducing snowboarder caused deropements.
The H-Bar
Validation Testing Procedure
Select several (approx. 3-4) resorts with T-bar surface lifts from across BC.
Form a control group of skiers and snowboarders (approx. 20-30 of each) for each resort.
Outfit every other carrier on surface lift with prototype H-Bar design.
Control group rides both original design and prototype design in different combinations of skier and boarder.
Observer rides behind each set of people in control group to observe sideways motion in each case.
Have each member of control rate Yes or No for increased comfort in each combination of riders.
If new design is considered more comfortable and manageable for the test subjects, the new design is a success.
References
http://www.abc-of-snowboarding.com/pistelifts.asp
http://www.faigle.eu/products-solutions/industry-solutions/general-liftingconveying-systems/ski-lift-t-bars.aspx
http://www.custompartnet.com/estimate/injection-molding/
CSA Z98-14 Standards Manual
Current
T-Bar Design
Benefits & Features
Same material, new design
Easy implementation
Cost effective
More comfortable
Less awkward rider stance
Reduces horizontal motion of snowboarders
Unique design accommodating snowboarders
New H-Bar Design
skiers
snowboarders
Rider Orientation Options
Direction of
Movement
Cost Requirements (Dollars per H-Bar)
Material requirements: 500-700
Injection moulded and extruded aluminum
Impact and cold shock resistant polypropylene
Manufacturing Requirements: 200-300
Installation Requirements: 100-200
Lift Shutdown Cost: 200-400
Total: $1000-1600 per H-Bar